Plastimatch Users Guide

Gregory C. Sharp
Revision 278
March 19, 2009

# Users documentation
## Downloading the code

The web site at plastimatch.org has instructions on how to download the code.
## Description of programs

These are all written in C or C++, and run on Windows or Linux.

Name	Purpose
analyze_to_mha	Converter
compose_vector_fields	Compose two vector fields
contour_statistics	Compare contours using DICE or other statistics
cxt_to_mha	Render a CXT file into a binary MHA
dicom_to_mha	Converter
dicom_uid	Make a new, unique dicom UID
drr_c	Generate DRR from image volume
fdk_c	Perform FDK cone-beam reconstruction
mask_mha	Mask out a portion of an image
merge2	Compose affine and vector field (obsolete?)
merge_vfs	Combine two vector fields (e.g. moving and non moving)
mha_to_analyze	Converter
mha_to_raw	Converter
mha_to_rtog_dose	Converter
mha_to_vox	Converter
patient_mask	Generate binary mask for patient boundary
plastimatch	Main registration program
point_path	Fast point trajectory solver
raw_to_mha	Slap an MHA header onto a RAW file
resample_mha	Crop, resize, or resample 3D image or vector field
rtog_to_mha	Converter
shuffle_mha	Reshuffle (x,y,z) axes in certain ways
tps_interp	Make a VF from a set of landmark correspondences
tps_update	Modify registration with thin-plate spline
union_mask	Combine masks with union operation
vf_compare	Compare two vector fields
vf_stats	Print statistics of a vector field
vf3d_to_mha	Converter
vox_to_mha	Converter
warp_dij	Apply a vector field to a dij file, creating a new dij file
warp_mha	Apply a transform (rigid, affine, bspline, or vector field) to a 3D image, create a new 3D image
warp_pointset	Apply a transform to a list of points
xf_to_xf	Converter, can convert XF to VF, or XF to XF

The following driver programs are available. They are used for development.

Name	Purpose
bspline	Run native B-spline registration
demons	Run native demons registration

The following scripts are available. They are written in perl, batch, or matlab. Not every utility program is listed.

Name	Purpose
cms_to_mha	Matlab converter
read_mha	Matlab program to load MHA format
write_mha	Matlab program to save MHA format
write_nrrd	Matlab program to save NRRD format
patient_mask	Matlab program to generate a patient mask if it is missing

## Quick Start Guide

How to run registrations

1) Convert dicom to mha
    Edit and run convert_4dct.pl

2) Fix the problem with RPI -> RAI orientation in the header.
    Edit and run fix_orientation.pl
    (This is not necessary for ITK 2.4.1)

3a) Make masks from cms contours
    Edit and run render_cms_contours.m
    You have to manually rename these for dp-series sets

3b) Make masks from ge contours
    Edit and run render_cms_contours.m
    You have to manually rename these for dp-series sets

4) Subsample mha & mask separately
    Edit and run subsample_mhas.pl
    Then, edit and run subsample_mhas.bat

5) Apply masks
    Edit and run apply_mask.pl
    Then, edit and run apply_mask.bat

6) Run registration
    Edit and run bspline.pl
    Check bspline??.bat, and parms??_??.bat

## Example registration parameter file
## Comments begin with '#', blank lines are ignored
## A "GLOBAL" section is required, and specifies the inputs
## and optional outputs.
##
## For the output files, it is similar, but not exactly the same
## as putting them in the last stage.
##
## The use of xform_out is undefined when xform=vf,
## such as demons registration. Use vf_out instead.
[GLOBAL]
fixed=t0p_221.mha
moving=t5p_221.mha
xform_in=my_bsp.txt
vf_out=my_output_vf.mha
xform_out=my_output_bsp.txt
img_out=my_output_img.mha

## Use a "STAGE" section for each stage of processing.
## You can get outputs (vf_out, xform_out, and img_out) if
## you like.
## Default values will be used for each option unless you
## override them here.
[STAGE]
xform=bspline
optim=lbfgsb
# Use GPUIT implementation
impl=gpuit_cpu
# Use ITK implementation
impl=itk
# Quit after 50 iterations
max_its=50
# Quit if change in score differs by less than 3
convergence_tol=3
# Quit if gradient norm is less than 0.1
grad_tol=0.1
# B-spline grid spacing (in mm)
grid_spac=30 30 30
# Subsample by 4,4,2 in x,y,z directions
res=4 4 2
# At the end of this stage, output the final xform
xform_out=stage_1_output_bsp.txt

## For each subsequent stage, add another "STAGE" section.
## You only need to include parameters that you want to change.
## Any unspecified parameter is inherited from the
## previous stage.
[STAGE]
max_its=20
convergence_tol=4
grad_tol=0.2
res=2 2 1

## To run demons, set optim to "demons" and xform to "vf."
[STAGE]
xform=vf
optim=demons
impl=itk
vf_out=output_2.mha

## If you want to, you can use a "COMMENT" section
## to comment out a stage.
[COMMENT]
xform=bspline
max_its=200

## GPU acceleration requires brook
[STAGE]
optim=demons
xform=vf
impl=gpuit_brook
res=4 4 2
max_its=200
# Std dev of smoothing kernel (in mm)
demons_std=10
# "Gain" factor, higher gains are faster but less robust
demons_acceleration=5
# Homogenezation is the tradeoff between gradient
# and image difference. Values should increase for larger
# voxel sizes, going down to about 1 for 1mm voxels.
demons_homogenization=30
# This is the size of the filter (in voxels)
demons_filter_width=5 5 5
## Listing of registration parameters
The parameter file has two sections: a GLOBAL section at the top of the file, and one or more STAGE section. Parameters such as input files are put only in the GLOBAL section. Output files can be put in the GLOBAL section or any STAGE section (which will write out intermediate output).

option	stage	value
fixed	GLOBAL	Name of fixed image
moving	GLOBAL	Name of moving image
xform_in	GLOBAL, STAGE	Initial guess of transform
xform_out	GLOBAL, STAGE	Final solution, as transform
vf_out	GLOBAL, STAGE	Final solution, as vector field
img_out	GLOBAL, STAGE	Warped image
img_out_fmt	GLOBAL, STAGE	“auto” (default) Output format Must be either “auto”, which uses filename extenstion to determine, or “dicom”, which iterprets img_out as a directory name to output the dicom files
img_out_type	GLOBAL, STAGE	“auto” (default) / Data type of the output image, usually either float, short, or uchar
background_max	GLOBAL	-1200.0 (default) Units: image intensity / This is used to automatically determine a region of interest

Optimization parameters. There are three key parameters that decide which algorithm is used for optimization.

xform	optim	impl
translation	rsg amoeba	itk
rigid	versor amoeba	itk
affine	rsg amoeba	itk
vf	demons	itk gpuit_cpu gpuit_brook
bspline	steepest lbfgs lbfgsb	itk gpuit_cpu

Notes:

1. Default values are: xform=rigid, optim=versor, impl=itk.
2. Amoeba is reported not to work.
3. B-spline with steepest descent optimization is only supported on gpuit_cpu implementation.
4. B-spline with lbfgs optimization is only supported on itk implementation.

The following specific parameters are used to refine the optimization. Depending on the choice of xform, optim, and impl, a different set of specific parameters are available.

option	xform+optim+impl	value
res	any+any+any	[4 4 1] (default) / [1 1 1] (minimum) / Units: voxels / Must be integers
metric	any+not demons+any	mse (default) / mse, mi, mattes (impl=itk) / mse, mi (impl=gpuit_cpu)
background_val	any+any+any	-999.0 (default) / Units: image intensity
min_its	any+any+any	2 (default) / Units: iterations
max_its	any+any+any	25 (default) / Units: iterations
convergence_tol	any+not demons+any	5.0 (default) Units: score
grad_tol	any+{lbfgsb or lbfgs}+any	1.5 (default) / Units: score per unit parameter
max_step	any+{versor or rsg}+itk	10.0 (default) / Units: scaled parameters
min_step	any+{versor or rsg}+itk	0.5 (default) / Units: scaled parameters
grid_method	Bspline+any+any	Obsolete
mi_histogram_bins	any+any+any	20 (default) / Number of histogram bins / Only for gpuit or itk Mattes mutual information
mi_num_spatial_samples	any+any+itk	10000 (default) / Number of spatial samples. / Only for itk Mattes mutual information
num_grid	Bspline+any+any	Obsolete
grid_spac	Bspline+any+any	[20. 20. 20.] (default) / Units: mm / Must be not less than 4*(Pixel Size) in case of GPUIT implementation. Should not be that small for ITK either.
histoeq	vf+demons+ITK	0 (default) / Not used. Means don't equalize intensity histograms.
demons_std	vf+demons+any	6.0 (default) Units: mm
demons_acceleration	vf+demons+GPUIT	1.0 (default) / Units: percent
demons_homogenization		1.0 (default) Units: ??
demons_filter_width		[3 3 3] (default) Units: voxels

## CXT File Format
The cxt file format is an ASCII format that mirrors the DICOM-RT structure set format. The perl utility make_dicomrt.pl converts from CXT to DICOM-RT.
The following sections
Header section	Various flexible ascii fields
ROI section	List of ROI's in the structure set, along with a fixed set of information on each
Contour section	List of contours, with a fixed set of information about each

The header section contains mostly information about the associated volume:
SERIES_CT_UID uid	The uid field specifies the UID for the associated CT volume
OFFSET x y z	The x y z fields specify the position of the first (upper left) voxel in the image
DIMENSION x y z	The x y z fields specify the size of the volume
SPACING x y z	The x y z fields specify the inter-voxel spacing

Each line of the ROI section contains three fields, separated by the ASCII space “ ”.
Field	Value	Example
Number	A postitive integer	1
Color	RGB tuple, separated by backslashes	0\255\0
Name	ascii string	gtv_primary

Each line of the contour section has 6 fields, separated by the pipe symbol “|”.

Field	Value	Example
ROI Number	A postitive integer, referring to the ROI	1
Contour thickness	This is used by GE. Not sure how useful it is	2.5
Number of points	How many points in the contour?	3
Slice index	Which slice does this contour belong to within the CT series of interest? The numbering start with 0 for the first slice sorted by Z.	20
Associated slice UID	Which slice does this contour belong to within the CT series of interest?	2.16.840.1.114362.1.90609.1196125535718.935
Points	Sequence of x\y\z tuples, separated by backslashes. Units are mm. z value should be the same for all of the points.	5.4\-63.2\10\8.4\-66.2\10\1.8\-49.0\10

## DICOM Conformance
Obviously, this section is under development.

The DICOM prefix for plastimatch is 1.2.826.0.1.3680043.8.274.1. This is a subrange of the prefix 1.2.826.0.1.3680043.8.274 which was assigned by Medical Connections.

Plastimatch defines UIDs the following sub-subrange(s). All other uses are reserved.

1.2.826.0.1.3680043.8.274.1.Y.ZZZZZZZZZZZZ

Y = 1	Reserved for non-clinical data (phantoms, special projects, software development)
Y = 2	Clinical data
Z	Up to 33 digits and dots

Plastimatch uses two different dicom engines. GDCM for itk-related routines, and DCMTK for perl-related routines. These engines have different default conformance properties.

### CT Export in plastimatch

IE	Module	Reference (Dicom 2004)
Patient	Patient	C.7.1.1
Study	General Study	C.7.2.1
Series	General Series	C.7.3.1
Frame of Reference	Frame of Reference	C.7.4.1
Equipment	General Equipment	C.7.5.1
Image	General Image	C.7.6.1
	Image Plane	C.7.6.2
	Image Pixel	C.7.6.3
	CT Image	C.8.2.1
	SOP Common	C.12.1

Patient Module
Attribute Name	Tag	Type	Notes
Patient Name	(0010,0010)	2
Patient ID	(0010,0020)	2
Patient's Birth Date	(0010,0030)	2	No value assigned
Patient's Sex	(0010,0040)	2	No value assigned

Frame of Reference Module

Attribute Name	Tag	Type	Notes
Frame of Reference UID	(0020,0052)	1
Position Reference Indicator	(0020,1040)	2	No value assigned

### RT Structures
To be written.
### RT Dose export
To be written.