Deformable registration programs

Gregory C. Sharp
Revision 225
January 7, 2009
# Developers notes

This section will be of no use anyone. It is just my random notes.
## Xform conversion
Mainline converters

xform_itk_bsp_to_itk_bsp	Resample itk bspline at new grid spacing using method from itk example code. How this works is not fully documented.
xform_gpuit_bsp_to_itk_bsp	Convert gpuit bsp to itk bsp by copying coefficients, then call xform_itk_bsp_to_itk_bsp to resample at new grid spacing.

Auxiliary functions

itk_bsp_extend_to_region	Extend the itk bspline to add zero valued control points at outside of region.
gpuit_bsp_region_to_itk_bsp_region	Change region flavor.
gpuit_bsp_to_itk_bsp_raw	Change bspline data structure without changing region or grid spacing.

There is a Xform wrapper around the GPUIT structure. This was needed when the GPUIT code was a separate library, but is no longer needed?

The xgb values are set at the beginning of the stage. They are given exactly the same values as parms.
It is used in two places. gpuit_bsp_to_itk_bsp_raw and xform_gpuit_bsp_to_gpuit_bsp

Regarding the conversion to final full-sized vector field, the two methods use different conversion chains.
The traditional ITK chain uses:
xform_to_itk_vf
xform_gpuit_bsp_to_itk_vf
gpuit_bsp_to_itk_bsp_raw
itk_bsp_extend_to_region
xform_itk_any_to_itk_vf
save_warped_img_itk
The GPUIT chain uses:
xform_to_gpuit_vf
volume_create
bspline_interpolate_vf
save_warped_img_gpuit

There is no (good) reason for the two methods to yield different vector fields, but they do.

bspline_interpolate_vf needs to be changed to allow arbitrary rendering.

## Aligned B-Spline registration

GPUIT B-spline registration uses a grid alignment technique and a data structure that greatly improves the computation speed of B-spline registration. The basic idea is to align the B-spline grid with the voxel grid, as shown in Figure 1. In this configuration, the position of each B-spline control point lies at the center of a voxel within the image. The control points are equally spaced, which partitions the volume into equal sized tiles. This partition into equally sized tiles is important to the approach, because it allows the coefficient multipliers used for B-spline interpolation to be precomputed.
The B-spline interpolation equation for cubic B-splines in 3-D is given as
<< equation here >>
where v(x, y, z) is a single component (e.g. the x component) of the displacement for a voxel located at (x, y, z). The P array contains the B-spline coefficient values that need to be optimized, while Ni, Nj, and Nk refer to the 1-D B-spline basis functions evaluated at x, y, and z respectively. A direct implementation of this equation requires 192 multiplications and 63 additions to solve v at each voxel location (x,y,z). This computation can be made much faster through grid alignment.
The (x,y,z) location is the equation above is measured relative to the B-spline base knot.  As shown in Figure 1, the voxel at (2,7) has a relative coordinate of (2,3).  By restricting the grid to be aligned, we limit the set of possible values for the product Ni(x)Nj(y)Nk(z).  This product is precomputed for each offset location within a tile, and reused tile by tile.
An illustration of the data structure needed to support this technique is shown in Figure 2.  The data structure consists of 4 tables: the coefficient array, the gradient array, the multiplier lookup table (LUT), and the index LUT.  Each voxel index is separated into its tile and offset coordinates as shown in Figure 1.  Using the index LUT, the voxel can find the 64 coefficient valuesof the B-spline control points associated with the voxel.  The multiplier LUT holds the 64 corresponding values of Ni(x)Nj(y)Nk(z), one for each control point.  To find the displacement vector for the voxel, therefore, would require looping through the 64 entries of each LUT, fetching the values, multiplying and accumulating.
The computation of the cost function gradient is done using the same data structures. For functions with analytic derivatives, such as mean squared error or kernel-based mutual information metrics, the gradient is updated by summing the contributions over each voxel.  These contributions are weighted by entries in the multiplier LUT and accumulated into the gradient vector.

## Optimization issues
There are issues with the optimizer. Some alternatives:
1. LBFGS
2. Libopt/modulopt
  1. fmincon: cuter
  2. lbfgs: cuter modulopt modulopttoys
  3. lbfgsb: cuter modulopt modulopttoys
  4. m1qn3: cuter modulopt modulopttoys
  5. n1cv2: modulopt modulopttoys
  6. n2qn1: cuter modulopt modulopttoys
  7. sqplab: cuter
3. Lancelot